Part numbers (TNR)	R1651 294 20
Size	25
Accuracy class	N
Preloading	without
Ball Chain	No
Seal	standard
Lubrication	pre-lubricated
A [mm]	70
A1 [mm]	35
A2 [mm]	23
A3 [mm]	23.5
B [mm]	86.2
B1 [mm]	57.8
H [mm]	36
H1 [mm]	29.9
K1 [mm]	12.45
K2 [mm]	13.6
K3 [mm]	5.5
K4 [mm]	5.5
H2 with rail seal cover strip [mm]	24.45
H2 without rail seal cover strip [mm]	24.25
E1 [mm]	57
E2 [mm]	45
E3 [mm]	40
E8 [mm]	38.3
E9 [mm]	11.5
N1 [mm]	9.3
N2 [mm]	7
N6±0,5 [mm]	15.2
S1 [mm]	6.7
S2 [mm]	M8
S5 [mm]	7
S9 [mm]	M3x5
T [mm]	60
V1 [mm]	7.5
weight [kg]	0.65
C [N] 1)	28600
C0 [N] 1)	35900
Mt [Nm] 1)	410
Mt0 [Nm] 1)	510
ML [Nm] 1)	290
ML0 [Nm] 1)	360
Note	Determination of the dynamic load capacities and moments is based on a travel life of 100,000 m per ISO 14728-1. Often only 50,000 m are actually stipulated. For comparison: Multiply values C, Mt and ML from the table by 1.26.
1) Note regarding the increase of the load capacities to be considered	Increased load capacities and load moments. Available from June 2, 2014 with production date FD 45402. Consecutive numbering indicates a subsequent date of manufacture. Maximum forces Fmax and moments Mtmax of profile rail guides according to catalog Ball Rail Systems R310.. 2202 (2014-12) on page 200-201, respectively to ISO 12090-1(DIN 637) have to be taken into account. General product information and mounting instructions in the catalog R310.. 2202 (2014-12) have to be considered. (Current catalog is available in Rexroth Media Directory)
Product group info	Note / Can be used on all Ball Guide Rails SNS.
Dynamic characteristics	Travel speed: vmax = 5 m/s Acceleration: amax = 500 m/s2 (If Fcomb > 2.8 · Fpr : amax = 50 m/s2)